## Slide 1: Remote Reading utilizing XDS-I infrastructure provided by Diagnostic Image Repositories

## Slide 2: X.1 Purpose & Scope
Attain efficiencies and reduce cost at a macro-scale level:
  Improve throughput of radiology depts by allowing any affiliated radiologist in the affiliated to read and report a study.
  Align the number of resources (staff, equipment) with the needs of the province as opposed to considering individual hospitals only.
  Facilitate assignment of studies to physicians that are best qualified to read them (e.g., a SPECT expert may be leveraged across the Jurisdiction)

## Slide 3: Remote Reads: Underlying Standards
XDS-I for hosting Images and reports
XDW underlying workflow profile framework
  Compatible with XDS/XDS-I architecture
  XDW currently does not support Cross community (XCA)
    Cross-Jurisdictional is out-of scope
    Workflow is all within the same affinity domain
    This will be addressed in context with IHE ITI community
XBeR-WD Workflow Definition
  Sufficient for Image Referral
XDR for point to point
  As necessary
DSUB for Notifications
  D-SUB can act as a notification mechanism for XDW results available/completed -OR- could be a trigger to receptionist to call Dr. XXX
Notes: -IHE XDW profile is being aligned better with XCA (get rid of folders, in favor of reference IDs)
-D-SUB being used for notifications
XDS/XDW only defines protocols about how to communicate images and reports. (plumbing) How the WORKFLOW Manager (usually a human, but could also be a business level workflow manager) assigns which exams to be read by whom and where and when. (brains)
Be careful not to give the false impression that implementing the plumbing (alone) will solve the problem.
The VA has this problem exponentially in the U.S.

## Slide 4: Systems
RIS
PACS
VNA
Community Image Sharing Network(Diagnostic Imaging Repositoy

## Slide 5: Use Cases for Consideration
Workload sharing
  Specialty reads (SPECT as an example)
  Site Loading
  Automated - someone out in the universe picks up the work item
  On-demand - set up in advance (eg., prior email conversation)
Double read (mammography example)
Consult
Blind Read
  May need to still consider VIP (de-identified) issues
Use case example: Specialty Read
  SPECT study is acquired in Toronto in a hospital A using RIS/PACS 1. The study needs to be read by a SPECT expert working at hospital B that uses RIS/PACS 2.
Notes: Need to be aware of over-read and double-read cases. This document may not address the correlation of the results between the outcomes of double-reads, for example.
Document very basic use case first, then look at variations.
Need to comment on where studies are read. e.g., remote browser or import directly into local PACS to be read.
Workflow Manager would update status of work item.
Use D-SUB to notify everyone of status changes. (e.g., back to originating RIS to initiate message to referring physician).
Differences in ability to approve report across jurisdictional boundaries. (credentialling) NOT part of this.

## Slide 6: Workflow Steps
  Remote Read Request
  Schedule Remote Read
  Remote Read
    Remote Read Subtasks
      Prep for Read
      Ready for Read
      Preliminary Read
      Final Read
  Read Complete
Notes: Steps which occur in reading:
Read Request (state = N)
Assign Read (state = A)
Import locally and prefetch, if necessary
Read Images (state = R)
Create new Evidence Documents, if applicable
Create Report (state = CR, whatever)
Approve Report (State = AP, whatever)

## Slide 7: Workflow Participants
Workflow Participants | Descritpion
Remote Read Requestor | Imaging Service (e.g., Hospital Radiology Department) that initiates and completes the Remote Read. Produces the request Read Request task and the related supporting document. This is the internal workflow monitor Accepts the remote read completion, completes billing cycle(out-of-scope)
Remote Read Scheduler | Participant responsible for scheduling the remote read by assigning a Specialist or Radiologist to perform the read (note it is presumed a single participant per affinity domain)
Remote Read Preparer | Participant responsible for importing Images to the local PACS. Including relevant priors, if necessary this is an optional role
Remote Reader | Participant responsible for performing the remote read. This workflow participant produces a preliminary report(optional), other collaborating evidence(optional) and final report to fulfill the read request and ending the remote read process
Workflow Monitor | Participant that tracks progress of the workflow and reacts to certain exception conditions. This participant can be standalone or grouped with one of the above Workflow Participants. Aware of the status of every single exam that is requested
Notes: Remote Request Reader
Remote Request Scheduler
Remote Request Performer
Workflow Monitor - often same as Remote Req Scheduler

## Slide 8: Process Flow: Input and output Documents for each task
Read Images
Input Documents Workflow Tasks Output Documents
Order
Image Manifest(S)
Clinical Summary
Read Request
Assign Read
Prep for Read
(Import locally if Necessary)
Read Complete
Images
Final Report
Evidence Documents
Final Report
Remote Read Req.
Image Manifest(S)
Clinical Summary
Exam/Tech notes
Exam/Tech notes
Remote Read Req.
Scheduled Read
Ready for Read
Preliminary Read
Final Read

## Slide 9: Process Flow: Input and Output Documents of each task/status pair
Task Type | Input Docs | Option | Task Status | Output Docs | Option
Remote Read Request | Imaging Service Order (HL7) | R | COMPLETED | Remote Read Request (CDA) Image Manifest(DICOM) Clinical Summary (CDA) Exam/Tech Notes (CDA) | R R O O
Schedule Remote Read | Remote Read Request(CDA) | R | IN-PROGRESS |  | 
 |  |  | COMPLETED | Remote Read Scheduled(HL7) | R
 |  |  | FAILED | Reason For Rejection | R
Read Images (may be broken down to subtasks) | Remote Read Scheduled(HL7) Image Manifest(DICOM) Images(DICOM) Clinical Summary (CDA) Exam/Tech Notes (CDA) | R R R C O | READY | Create local Temp Read Patient ID Instance Availability Notification | (local) (local)
 |  |  | IN-PROGRESS | Preliminary Image Report CAD Processing DICOM Evidence Documents | C C C
 |  |  | COMPLETED | Final Image Report | R
 |  |  | FAILED | Reason For Rejection | R
Read Complete | Final Report | R | COMPLETED | Imaging Service Order Complete (HL7) Final Report | (local) R

## Slide 10: Initiate request for remote read
  Automatically
    all studies acquired after certain time
    carrying certain procedure code
    Include a certain urgency code
    Peer review
    Remote Locum read
    VIP read (pseudo-anonymous)
    Double Read
  Manually
    Excessive read workload -for a site
    Specialty Consultant/Second read – directed to a person or specialty pool
Notes: Time stamp standardization is important so that Workflow Monitor can look across all systems.
Assign read to category (anyone reading XRs) or specific radiologist.
Manual v. Automated work assignments possible:
Pull v. Push - Radiologist can request any open studies to be read. Or, a case
can be assigned (pushed) to a specific radiologist. (esp important for SPECT cases, PET, etc.)
Business level logic and Business Agreements (e.g., all chest XRs will be read within 30 minutes) are implemented by the Workflow Monitor, not implemented in software/XDS. (Business Agreement part of policy, not enforced through systems today.)
Local read list can (but does not have to) be integrated with remote read list (integrated worklist or separate worklist). Local RIS/PACS still implements local worklist.

## Slide 11: Use Case Step 1: Initialize Workflow Specialty SPECT Read
The hospital has a NM acquisition system fully capable of acquiring SPECT Images, but lacks a credentialed NM Radiographer to read SPEC. Per the institutional business rules, all SPECT images will require a NM credentialed Radiologist to perform the read.
We have a list of credentialed readers
Targeted request - to a specific resource or resource pool or
Broadcast – not constrained to credentialed NM Readers for facility, not feasible in Canada today
Single scheduler for an affinity domain
XDS with scheduler subscribed to document type code or
Direct to scheduler

## Slide 12: Read Request
The Read Requestor, usually a department scheduler, for each study meeting the criteria for the read, creates a Remote Read Request.
This request includes automated or manual collection of information such as the original order information, acquired Images and other relevant clinical information. It would contain any read constraints.
Constraints/Conditions
      Must be read by…(time/date) part of BA policy
      Assigned to…(person, specialty, credentialed list who could be assigned)
      Upon read assigned (Acceptance), report must be released by.. (time/date)
      preliminary read requested(if needed), report must be created by (time/date)
    OUTPUT:
      Workflow Document Created (R)
      Manifest of Acquired Images (R)
      Remote Read Request (R)
      Clinical Summary (e.g. Referral) with reason for exam, patient history, requisition, etc (O)
      Exam/Tech notes, to include observations during scan (O)
    INPUT DOCUMENTS:
      Order: HL7 OMG, OMI or ORM
  Workflow Monitoring Requirements
    Monitor uses the constraints to monitor compliance
Constraints: All Output documents are linked via Accession Number
study needs to be removed from local reading list

## Slide 13: Schedule Remote Read
The Remote Read scheduler evaluates the request and assigns a reader
to read the SPECT Images based on the constraints and availability of resources.
INPUT DOCUMENTS:
  Read Request
  Workflow Document
Activity:
    Schedules read with local reading system
    The remote enterprise may need to create a local identity for that patient in order for the remote PACS to perform a read.
OUTPUT:
  Scheduled Read Confirmation
    Confirms it can complete the read request, on business agreement/constraints
    Error condition: Request for more information (no image set,, etc)
Workflow Monitor Requirements
  Load balance- The reading site may be allowed to have a specific loading number allowed

## Slide 14: Read Images
Specialist reading the SPECT Images selects the study. Specialst may create new DICOM evidence documents to
INPUT DOCUMENTS:
  Clinical Summery (e.g. Referral or original order) with reason for exam, patient history, etc
  Acquired Images (Image Manifest)
  Reconstructed Image Set (Image Manifest)
  Relevant Priors (Image Manifests)
  Exam/Tech notes (observations during scan)
  Workflow Document
OUTPUT:
  Evidence Documents Manifest(C)
  Post-processing Images Manifest (C)
  Final Report-signed (R)
  Error condition:
    Request for more information or
      incomplete image set,
      Poor Quality Images, Retake request
    cancel with reason, or
    re-assign
Monitor Requirements

## Slide 15: Read Subtask: Prep for Read
Once the Order for reading is accepted, the reading site may require the images and other relevant information to be imported into the local facility’s PACS or Reading Workstation. SPECT Images in particular, generally require specific reading and analysis tools not available in a general purpose image viewer.
INPUT DOCUMENTS:
  Acquired Images (Image Manifest)
  Relevant Priors (Image Manifests) and Reports (CDA)
Activity:
Imports foreign exams to local PACS or workstation, as necessary
OUTPUT:
Completes subtask(not necessarily reported to the XDS environment)
Error condition: Request for more information (image set not available,, etc)
Workflow Monitor Requirements: BA parameters monitoring

## Slide 16: Read Subtask:- Preliminary Read
INPUT DOCUMENTS:
  Same as previous
OUTPUT:
  Workflow Document Updated
    New evidence documents added
  Image Manifest
    imaging (DICOM) objects like secondary captures, presentation states, key object selections, structured reports, etc.
    New evidence documents with identical Accession number referenceID
  Preliminary Imaging Report
Monitor Requirements
Constraints:
Notes: Where do results (EvDoc + report) go back to? ED can be a.) sent back to originating site or b.) have access to the images from the DI-r. Send report back to originating source or send back to DI-r???? what about ED?
Report and image updates (evidence documents) is
Ideally, from a systems architecture point of view, the referring physician should access the report (read remote) from the DI-r, not the local RIS or the remote RIS (where the study was actually read).
Local RIS may need specific message to close local workflow (close order).

## Slide 17: Read Complete (Requestor Actor)
INPUT DOCUMENTS:
  Final Report
OUTPUT:
  Workflow Document Updated – closed
  Imaging Service Order Complete(HL7)
  Final Report sent to local system
Monitor Requirements
Constraints:
  Report needs to go direct to the Ordering facility in order to complete the workflow and the professional services workflow.
Notes: Are there LEGAL requirements to store the report back to the local RIS? (unintended consequences)
Rename XDS IG Appendix to "Transition Strategy". (for installed base systems)
Leaning heavily towards storing report back to DI-r. If an amendment is made, how will "the system" know all of the places the report has been sent to update all of them? Define the future direction.
The person who reads the report is responsible for approving the report. Today, the creation and the approval almost always happens at the same time. Exception may be teaching hospital (interns), but that is a different use case.
What if the patient does not exist in local PACS system? Can we use import codes from IRWF.b. This is a transition issue with existing PACS systems. The patient is not actually at this hospital or for patient care, the images are just there to be read.

## Slide 18: Thank you

## Slide 19: Remote Reporting Workflow Document Outline
Contents
  Introduction to this Supplement
  Open Issues and Questions
  Closed Issues
Volume 1 – Profiles
X Remote Read Workflow Definition (RR-WD) Profile
X.1 Purpose and Scope
X.2 Process Flow
X.3 Workflow Participants and Process Flow
X.3.1 Use Cases
X.3.2 Options
X.4 Workflow Definition Actors and Options
X.4.1 Workflow Definition Actors
X.4.2 Workflow Options
X.4.3 Workflow Definition Profile Grouping with other Profiles
X.5 Security Considerations

## Slide 20: Volume 2 – Content Modules
Y.1 RR Workflow Definition – XDW Workflow Document – Common Attributes
Y.2 XDW Content Modules
Y.3 Tasks Specifications
Y.3.1 Task: Read Request
Y.3.X Task:
Y.3.X Task:
Y.4 Input and output documents
Appendix A - Complete example of Remote Reporting Workflow Document
Appendix B - Technical development of WD related to the Remote Read process